## Slide 1: Barnes Lake 2022 Watershed Management Plan
Prepared for the Barnes Lake Property Association
Submitted By: Ashlee Haviland
June 16, 2023

## Slide 2: Components
Information gathering
Lake water quality
Inlet/Outlet water quality
BioSonics mapping

## Slide 3: Introduction
Lake is approx. 149 acres
Part of the Crystal Creek watershed
Part of the North Branch Flint River watershed
Barnes Lake watershed drains approximately 1,550 acres (2.4 sq. mi.)

## Slide 4: Goals & Objectives
Stable & diverse ecosystem (plants, fish, water quality)
Prevent & control invasive species
Reasonable recreation with minimal impact
Utilize best management practices
Recommendations

## Slide 5: Land Use
Deciduous Forest
33%
Wetlands
22%
Crops
9%

## Slide 6: Hydrology
Watershed contains mostly sandy soils
Better infiltration = better filtration, less erosion
High water table = “limited” soils

## Slide 7: Aquatic Plant Management
Four (4) Treatments in 2022
All targeted Aquatic Invasive Species (AIS)
  Starry Stonewort
  Eurasian Milfoil
  Curly-Leaf Pondweed
Date | Species Targeted | Acres | Product
April 28, 2022 | Starry stonewort, curly-leaf pondweed | 27.0 | Chelated Copper, Hydrothol 191, Aquathol K
May 31, 2022 | Eurasian watermilfoil, curly-leaf pondweed | 46.4 | Diquat Dibromide, Aquathol K
June 15, 2022 | Starry stonewort | 33.0 | Chelated Copper, Hydrothol 191, Flumioxazin
August 30, 2022 | Starry stonewort | 28.5 | Copper Sulfate, Hydrothol 191, Flumioxazin

## Slide 8: Inlet Water Quality
April sampling (High Flow)
  Phosphorus 14.2 ppb <80 ppb (EPA)
  Nitrogen 0.4 ppm <0.6 ppm (EPA)
  TSS 7.5 ppm <25 ppm (AFS)
  Turbidity 3.9 NTU <10.4 NTU (EPA)
  Conductivity 498 uS 150 – 800 uS (AFS)
  Flow Rate 4.75 cfs
        (2,131 gpm)

## Slide 9: Inlet Water Quality
July sampling (Low Flow)
  Phosphorus 22.5 ppb <80 ppb (EPA)
  Nitrogen 0.8 ppm <0.6 ppm (EPA)
  TSS 4.0 ppm <25 ppm (AFS)
  Turbidity 3.2 NTU <10.4 NTU (EPA)
  Conductivity 607 uS 150 – 800 uS (AFS)
  Flow Rate 0 cfs

## Slide 10: Lake Water Quality
Date | Location | Depth(ft) | Total Phosphorus (ug/L) | Free Reactive Phosphorus (ug/L) | TN (mg/L) | TKN (mg/L) | Conductivity (uS/cm) | Nitrate (mg/L) | Nitrite (mg/L) | Total Nitrate and Nitrite (mg/L) | Chlorophyll a (ug/L) | Total hardness (mg/L as CaCO3) | pH | Alkalinity (mg/L as CaCO3) | Secchi
4/21/2022 | A | Top | 15.0 | <5 | 0.6 | 0.6 | 454 | <0.02 | <0.02 | <0.02 | <10 | 186.6 | 8.4 | 162.9 | 13 feet
 |  | Middle | 32.1 | <5 | 0.5 | 0.5 | 451 | <0.02 | <0.02 | <0.02 | <10 | 185.7 | 8.4 | 164.9 | 
 |  | Bottom | <10 | 5.0 | 0.5 | 0.5 | 448 | <0.02 | <0.02 | <0.02 | <10 | 184.6 | 8.4 | 162.1 | 
 | B | Top | 16.8 | <5 | 0.5 | 0.6 | 463 | <0.02 | <0.02 | <0.02 | <10 | 198.2 | 8.4 | 172.7 | 
Date | Location | Depth(ft) | Total Phosphorus (ug/L) | Free Reactive Phosphorus (ug/L) | TN (mg/L) | TKN (mg/L) | Conductivity (uS/cm) | Nitrate (mg/L) | Nitrite (mg/L) | Total Nitrate and Nitrite (mg/L) | Chlorophyll a (ug/L) | Total hardness (mg/L as CaCO3) | pH | Alkalinity (mg/L as CaCO3) | Secchi
7/12/2022 | A | Top | 12.2 | <5 | 0.7 | 0.7 | 427 | <0.02 | <0.02 | <0.02 | <10 | 139.4 | 8 | 118.6 | 12.9 feet
 |  | Middle | 23.1 | <5 | 0.7 | 0.7 | 432 | <0.02 | <0.02 | <0.02 | <10 | 192.3 | 8.2 | 165.1 | 
 |  | Bottom | 36.3 | <5 | 2 | 2.0 | 410 | <0.02 | <0.02 | <0.02 | 18.2 | 178.0 | 8.2 | 149.5 | 
 | B | Top | 13.9 | <5 | 0.6 | 0.6 | 381 | <0.02 | <0.02 | <0.02 | <10 | 163.3 | 8.7 | 136.9 | 

## Slide 11: Temperature & Dissolved Oxygen Profiles
Chart: Temperature and Dissolved Oxygen Profile Site A April 21, 2022
| 46.94 | 46.760000000000005 | 46.760000000000005 | 46.760000000000005 | 46.760000000000005 | 46.94 | 46.94 | 47.120000000000012 | 47.120000000000012 | 46.94 | 47.120000000000012 | 46.94 | 46.94 | 46.58 | 46.58 | 46.94 | 46.94 | 45.32 | 44.96 | 45.32 | 44.96
Temperature (F) | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Dissovled Oxygen (mg/L) | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Minimum DO | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40

## Slide 12: Temperature & Dissolved Oxygen Profiles
Chart: Temperature and Dissolved Oxygen Profile Site A July 12, 2022
| 77.900000000000006 | 77.72 | 77.539999999999992 | 77.539999999999992 | 77.539999999999992 | 77.539999999999992 | 76.64 | 76.099999999999994 | 66.56 | 61.879999999999995 | 56.660000000000004 | 53.96 | 51.8 | 50.18 | 49.1 | 47.660000000000004 | 47.3 | 47.120000000000012 | 46.04 | 45.5 | 45.5
Temperature (F) | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Dissovled Oxygen (mg/L) | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Minimum DO | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40

## Slide 13: BioSonics - Bathymetry

## Slide 14: BioSonics – Plant Biomass

## Slide 15: BioSonics - Substrate

## Slide 16: Watershed SWOT
  STRENGTHS
  Small watershed
  Limited agriculture
  Plentiful wetlands & forest
  Excellent water quality in the lake

## Slide 17: Watershed SWOT
  WEAKNESSES
  Established invasive species
  Septic systems surrounding lake
  Roads present source of pollution

## Slide 18: Watershed SWOT
  OPPORTUNITIES
  Continue monitoring
  Better management of AIS
  Implement new projects to protect & improve lake WQ

## Slide 19: Watershed SWOT
  THREATS
  Development
  Failing Septics
  New introductions of AIS
  Boat traffic

## Slide 20: Action Plan – Future Possibilities
  Similar study in the future
    Continue monitoring water quality
  Aquatic Plant Management (APM)
  AVAS Surveys
  Biological monitoring of inlet & outlet
  Fishery survey

## Slide 21: Recommendations for Riparians
  Limit development, especially shoreline
  Improve shoreline habitat
    Low-profile prairie grasses
    Add native species around seawalls
  Replacing seawalls
  Stop the spread of AIS
  Responsible lawn care (fertilizer & clippings)
  Buffer stormwater drainage
  Obey No-Wake zones

## Slide 22: Options for Lake Board
  Systemic herbicide for Eurasian Milfoil
  Early treatment for Curly-Leaf Pondweed
  Starry Stonewort: aggressive & often
  Nutrient Mitigation Treatment
  Drawdown
  Inlet Settling Basin

## Slide 23: THANK YOU!
  Pete Filpansick
  SOLitude Lake Management
  3390 N State Rd, Suite D
  Davison, MI 48423
  Pete.Filpansick@solitudelake.com
  www.solitudelakemanagement.com